## Slide 1: MediaServer C Series
Multi-channel SD/HD/4K Video Server
Notes: Rev002
Date: 2016/01/15
Add 2In2Out in the table in Page5.
Add description “Support for graphic like logo, image” in Page6.
Rev 001
Date: 2015/01/26
Update storage drives and features

## Slide 2
Baseband
Studio
Outside
Broadcast
Live
Automation
3rd Party
Automation
Traffic System
3rd Party
Traffic System
Media Server C
Ingest
NetDisk
Journalist
Videos / Images
Production/MAM
AVID
FCP
DALET
ADOBE
PREMIERE
Cloud Aqua
Play Back
LAN/WAN
Media Server C
Play to Air (SD/HD/4K)
FTP
HTTP
SMB2
SMB2
API/VDCP
API/VDCP
Playlist Preload
XOR Media
Controller
Tool
Video clips/
Templates
Live
feed
XOR Media Architecture
SDI
IPTV
IP Stream
CDN
Cloud Aqua
3rd party Cloud
SMB2

## Slide 3: MediaServer C Series
Multi-channel SD/HD/4K Video Server
Notes: Low Cost
o ~50 cents/GB (can go lower if we make desktop-class SATA work stably with SHAS)
· High Density Architecture
o 2 heads (in non-HA configuration), each controlling 35 x 3.5” SAS/SATA drives, housed in a 4RU package
· Optimized ingest and streaming bandwidth
o Ext4 file system (multi-allocator and delayed allocation for simultaneous writes clustered into continuous layouts), SHAS write back cache and read ahead (for bursts of sequential writes/reads)
· Virtualized storage pool with NGOD support
o A3 for ingest and C2 for CDN transport, no external application or SRM necessary to determine content’s physical location
· Integrated RGB packager (for 3-screen formats)
o Allows RSDVR to be encoded in several bitrates of H.264 and then only packaged into FLV, HLS, etc. in real time when customers actually demands it from a mobile device
o Integrated recording software (RestarTV), integrate with EPG source to initiate recording based on EPG

## Slide 4: Hardware Components
3RU server chassis
System boot disk: SSD, 128GB or above
Redundant, hot-swappable power supplies
Up to 8 input/output ports
Video Storage Options:
  With UML N
  With local storage eight or sixteen 240GB/480GB/960GB/1.92TB/3.84TB (SSD) or 1TB/2TB/4TB/8TB (HDD)
RAID6 protection of HDD/SSD local storage (optional)

## Slide 5
SD/HD
  Maximum of 8 Playout Channels
  Maximum of 8 Ingest Channels
  The Configuration of the Codec Pack is ‘a la carte’
  Configurable as SD only or HD only or HD/SD switchable
  4K
  1 Playout Channel
  Support HD Up Conversion to 4K
I/O Configuration

## Slide 6
Software codec configuration for SD only or HD only, SD/HD switchable or 4K
Encode and decode support for multiple video formats
Support for up conversion, down conversion and cross conversion
Support for Close Caption and Teletext
Support for graphic like logo, image
Support for Aspect Ratio conversion
Support for VDCP, Sony and MCCAPI Control
Software Components

## Slide 7
Configuration Utility

## Slide 8
Perfect for direct ingest and playout
Embedded FTP server minimizing system fragmentation as much as possible (available for local storage)
Embedded SMG Lite for file ingest/file transfer (available for local storage)
Direct streaming with XOR UML N CloudAqua Storage
Multi-functionality

## Slide 9
High Density
  Easy to expand with increasing density requirements
High Reliability
  Redundant, hot-swappable power supplies
  Flash SSD boot disk for high-speed booting and extra reliability
  RAID6 protection against 2-drive failure
High Density and Reliability

## Slide 10
Support various media file formats
  Offers open media format supporting for MPEG-2, DV, MXF, QuickTime, MOV, DNxHD and AVC-Intra, etc.
  Back-to-back playout of multi-formats and multiplexes
Seamless Integration
  Communicates with third-party applications such as automation system via VDCP or API and media asset manager via API
  Works with XOR MediaController Application for recordlist/playlist scheduling and controlling
  Able to work with XOR UML N CloudAqua
Open Technology

## Slide 11
Scalability
  Beginning with 4 channels scalable up to 8 channels
  Upgrade Kit expands local storage capacity up to 128TB
HD-Capability
  Support for 8 HD channels of 1080i and 720p or 4 simulcast channels
  HD/SD switchable
  Support for up/down conversion and cross conversion
UHD-Capability
  Support for 1 UHD channel
  Support for HD Up Conversion
Technology Advances

## Slide 12
Broadcast Quality Server
A la carte channel configuration
Support for up/down and cross conversion
MPEG-2, DV, MXF, QuickTime, MOV, DNxHD, AVC-Intra and XAVC format support
Direct streaming with local storage or XOR UML N CloudAqua storage
Up to 128TB local storage
Highlights

## Slide 13: Thank you!
Notes: Low Cost
o ~50 cents/GB (can go lower if we make desktop-class SATA work stably with SHAS)
· High Density Architecture
o 2 heads (in non-HA configuration), each controlling 35 x 3.5” SAS/SATA drives, housed in a 4RU package
· Optimized ingest and streaming bandwidth
o Ext4 file system (multi-allocator and delayed allocation for simultaneous writes clustered into continuous layouts), SHAS write back cache and read ahead (for bursts of sequential writes/reads)
· Virtualized storage pool with NGOD support
o A3 for ingest and C2 for CDN transport, no external application or SRM necessary to determine content’s physical location
· Integrated RGB packager (for 3-screen formats)
o Allows RSDVR to be encoded in several bitrates of H.264 and then only packaged into FLV, HLS, etc. in real time when customers actually demands it from a mobile device
o Integrated recording software (RestarTV), integrate with EPG source to initiate